## Slide 1
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Some recent physics developments in COSMO for the ICON model
Updated droplet activation in connection with new aerosol input
COSMO-PP CAIIR
ART-component of ICON
Consideration of dissipation heating
TKE-feedback on Lower Limits of Diffusion Coefficients (LLDC)
Towards Empirical Hyper-Parameterization by Conditional Adaptive Parameter Tuning (APT)
COSMO-action ConSAT
Particular DWD initiative
Parameterization of micro-physical source terms (mainly excluding sub-grid heterogeneity):
Parameterization of macroscopic sub-grid heterogeneity:
Actions around Aerosols and Reactive Trace gases (ART)
Implementation of Spectral Bin Microphysics (SBM) as a reference

## Slide 2
September 2024 - August 2027
Total planed FTEs : 6.1
Participants:
Harel Muskatel (IMS)
Pavel Khain (IMS)
Euripides Avgoustoglou (HNMS)
Daniel Rieger (DWD)
Alberto de Lozar (DWD)
Piero Serafini (CETEMPS)
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Aerosol-CLoud Interactions in ICON Model (ACLIIM):
COSMO-Priority-Project
  PL

## Slide 3
extended particle-size range (even snow-flakes, hail-stones included)
  2D AOD-550nm climatology (Tanre, Tegen, MACv2 (Kinne), CAMS)
  assumed extinction coefficient
  grid-column integrated mass per m2
  mean particle-radius and -density
  assumed (exponent.) vertical decay
  local aerosol/dust number concentration (NCN in m-3), particle size distribution (mean and standard-deviation)
  number concentration of activated cloud droplets (CDNC)
  & effective updraft wind-speed:
  effective radius (Reff) of liquid clouds
  & cloud water content
  optical properties (as input for radiation): ext. coeff. (βext), single scat. alb. (ω), asymm. fact. (g), delta-transm. fact. (fd)
  Segal/Khain, 2006: 4D Look-Up-Table
  Hu et Stamnes, 1993
  (RG-COSMO, RRTM-ICON)
  Hogan et Bozzo, 2018
  (ecRAD-ICON:
  SOCRATES-package)
  & particle-size distribution
  number concentration of activated ice particles
  & mass-size relation
  effective radius (Reff) and aspect ratio of particles
  Ray-tracing for randomly distributed hexagonal or ellipsoidal particles (visible bands, Fu, 2007)
  Mie-scattering (IR bands, Fu, 1998)
  & temperature:
  DeMott, 2015 cloud-ice activation
  being further harmonized with
  1- and 2- moment microphysics
  direct aerosol effect
  online prognostic correction
  OFFline prognostic or climatologic 4D CAMS aerosols:
  Sulphate, Mineral Dust and Sea-Salt (3 size-bins each), Black Carbon, Organic Matter (hydro-phil. and -phob.)
  interpolation in space and time
  SGS variability
  SGS variability
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
  ONline prognostic 4D ICON-ART:
  dust, sea-salt and
  Biomass-Burning-aerosols
indirect aerosol effect introduced into ecRAD
Aerosol-CLoud Interactions in ICON Model (ACLIIM) in connection with ICON-ART:
  & hygroscopicity: ‘pyrcl’:
  Rothenberg/Wang, 2016
and
sub-grid
effects
  Mi-AI: AI-based ONline
  Mi-scattering
  as part of ICON-ART

## Slide 4
4
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
provided by Harel Muskatel (IMS)
ACLIIM: Optional Droplet Activation by ‘pyrcl’
  Segal/Khain, 2006: 4D Look-Up-Table
  + effective updraft wind-speed
  CDNC
  ‘pyrcel’: adiabatic cloud-parcel model,
  Rothenberg/Wang, 2016:
  numerical solution of 5 ordinary differential-equs.
  + initial state:
  updraft speed
  pressure
  temperature
  super-saturation
  CDNC & max. super-saturation
  ML-emulation:
  Wide & Deep Model
Wide and Deep ML architecture results:

## Slide 5
5
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
ACLIIM: General Aerosol-Effect:
  (scattering and absorption of LW/SW)
  (cloud albedo)
  (Reff)> (βext , ω) (g) => (optical depth)
  reduced/delayed auto-conversion () and precipitation
  longer cloud life
  direct radiation effect:
  indirect radiation effect:
  microphysical effect:
according to ACLIIM-Plan
  more aerosols

## Slide 6
6
Matthias Raschendorfer
provided by Harel Muskatel (IMS)
EWGLAM/SRNPW, Norrköping-Hybrid 2025
  CDNC (cm-3) at 35.0°N (15.0 – 26.0)°E – 06.09.2023 06:00
ACLIIM: Precipitation and CNCD
2D AOD-550nm climatology (with prognostic correction and constant Reff)
Precipitation (mm)

## Slide 7
7
Aerosols-Radiation: 2D AOD-550nm climatology
(with prognostic correction and constant Reff)
Aerosols-Radiation: CASM climatology
Aerosols-Radiation: CASM forecast
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
ACLIIM: Surface-Radiation
provided by Harel Muskatel (IMS)
Surface Radiation (W/m2)

## Slide 8
8
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
provided by Pavel Khain (IMS)
ACLIIM: Spectral Bin Microphysics in ICON
Mixed-Phase Spectral-Bin Microphysics (SBM)
  as a sophisticated reference
  66 bins: droplets + CCN tracers
  runs about 7-times slower than 1-mom scheme
Comparison of SBM against 2-mom scheme:
SBM shows reasonable behavior
strong sensitivity to CCN
Example:
  Cumulonimbus development (Weisman-Klemp 1982)
QC+QR (g/kg)
0
4
8
12
16
50km
Khain, P., J. Shpund, Y. Levi and A.P. Khain, 2022. Atmos. Res., 279, 106388.

## Slide 9: HErZ project (2023-2027)
9
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
provided by Ali Hoshyaripour (KIT)
Preparing ICON-ART for seasonal to decadal climate predictions in seamless regional to global model configurations
 ICON-Seamless + ART = ICON-SmART
Emissions of natural aerosols and trace gases from fully coupled and interactive ocean and land modules
Comprehensive atmospheric chemistry (troposphere and stratosphere) → optimization and acceleration
ML-based and scale-aware aerosol dynamics and washout
Multi-year simulation with full chemistry- and aerosol-treatment

## Slide 10: Preliminary results: aerosols
10
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
provided by Sanhita Ghosh and Pankaj Kumar (KIT)
Evaluation and acceleration in progress!

## Slide 11
11
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Thermodynamic coupling of Sub-grid Kinetic Energy (SKE) according to STIC :
  CKE
  TKE
  MKE
  PTE
  Shear/Form-Drag
  Dissipation
  Buoyancy
  SRE
  Radiation
  Potential Thermal Enthalpy
  Mean Kinetic Energy
  Spatial/Solar Radiation Energy
  Circulation Kinetic Energy
  D-SSO, SHS
  T-SSO, CON
Heating by dissipation of TKE has been neglected so far due to numerical problems
A stable approximation of dissipative heating (through neglecting the buoyancy impact) shows a significant impact!
  D-SSO: Dynamic SSO-scheme: induced sub-grid wakes and gravity waves
  SHS: Separated Horizontal Shear Eddies
  (part of TURBDIFF-code)
  T-SSO: Thermal SSO-scheme: sub-grid ana- and katabatic circulations (part of TURBDIFF-code, totally revised version in ICON-branch ‘mrturb’)
  CON: Convection scheme: buoyancy driven plumes
  Turbulent Kinetic Energy
Matthias Raschendorfer, Günther Zängl (DWD)
STIC: Separated Turbulence Interacting with NTCs

## Slide 12
12
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
STIC and the crucial impact of Lower Limits of turb. Diff.-Coeff. (LLDC):
  CKE
  TKE
production terms dependent on:
specific length scales
and a specific velocity
scale ( )
related to NTCs, such as:
SSO-generated wakes and thermals,
separated horizontal shear-eddies,
convective vertical currents
production terms depend on:
turbulent length scale and the turbulent velocity scale ( )
The scale interaction term shifts Sub-grid KE from the NTC part of the spectrum (Circulation KE)
towards the turbulent part (TKE) by virtue of shear
generated by the sub-grid circulation flow patterns.
NTC: Non-Turbulent SGS Circulation
STIC: Separated Turbulence Interacting with NTCs
TKE needs to be adapted to !
Excess of over is due to missing shear by NTCs
Excess of over is due to missing SGS pressure-
forces in momentum budget !!
with some empirical conditional scaling
turbulent diffusion coefficient:
stability function
turbulent master length scale
turbulent velocity scale
artificially limited by a LLDC
substituting not yet properly represented STIC-terms!
scalars like Heat
Momentum
Matthias Raschendorfer (DWD)
Additional TKE-production and dissipative heating

## Slide 13
13
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
  Quite large positive impact of “consideration of dissipative heating” in combination with “TKE-adaptation to LLDCs”
  (much more than expected)!
  Strong reduction of the long-standing cold-bias along the Antarctic cost during winter time
  Strong reduction of regional cold-bias during winter at the Northern Hemisphere
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Impact of STIC-corrections to NWP:
REF better
EXP better
Matthias Raschendorfer, Günther Zängl (DWD)

## Slide 14
14
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Impact of STIC-corrections to NWP:
EXP REF
REF. better
EXP. better
Matthias Raschendorfer, Günther Zängl (DWD)

## Slide 15
15
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Treating the long-standing moist and cold near-surface bias at late afternoon
A prototypic canopy scheme in the COSMO-model has already proven to cure the problem
Has not yet been implemented into ICON due to strategic reasons
revised TURBDIFF imported from ICON
+ new decoupled surface cover (canopy-scheme)
amplitude slightly overestimated
removed cold bias in the afternoon!
almost perfect double wave!
still some problems
during heating of the cover (stable stratification within the roughness layer)
T_2m
TD_2m
revised TURBDIFF
imported from ICON
direct analysis of
near-surface variables
Matthias Raschendorfer (DWD)
Cover from roughness-elements
with its own heat-budget
SAI-dependent number of semi-transparent layers
Thermal layer-coupling by
SHF and LRF
SAT from cover-layers according to generalized BLA

## Slide 16
16
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Approaching Hyper-Parameterization by Adaptive Parameter Tuning (APT):
  Time-filtered DA-increments of and at the lowermost model level
  Dominated by measurements of
  Proxies for local systematic error of (near-surface) and - amplitude
  Used as predictors for multiplicative empirical correction-factors for non-confident parameters:
  adapting to weather condition
  Land-use roughness and SSO blocking tendency
  Minimal evaporation resistances of bare soil and plant-stomata
  Heat-conductivity and -capacity
  Snow-albedo
  Minimal diffusion coefficient
  default value of (internal-global or external-local) parameter
  Hydraulic diffusivity of uppermost soil layer
  Albedo of snow-free land-fraction
  Scaling factor in snow-fraction diagnostics
  introduced last year
  i = 1 2 3 4
according to Günther Zängl (DWD)
  that appear to be dependent on the model state
  function of model state: hyper-parameterization
https://rmets.onlinelibrary.wiley.com/doi/10.1002/qj.4535

## Slide 17
17
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Consolidation of Surface-to-Atmosphere Transfer (ConSAT)
Reducing the moist and cold near-surface bias at late afternoon by conditional APT:
(SHFL+LHFL) < 0 .AND. SHFL > 0 => increasing laminar resistance of scalar SAT
(SHFL+LHFL) < 0 .AND. LHFL_bare_soil < 0.25*SHFL => increasing pore resistance for bare-soil evap.
Reduced (upward) evaporation (LHFL < 0) at late afternoon
EXP REF
REF. better
EXP better
Günther Zängl (DWD)
  by means of the predictor

## Slide 18
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Some recent physics developments in COSMO for the ICON model
Actions around Aerosols and Reactive Trace gases (ART)
Updated droplet activation in connection with new aerosol input
Implementation of Spectral Bin Microphysics (SBM) as a reference
Empirical Hyper-Parameterization by Conditional Adaptive Parameter Tuning (APT)
Parameterization of micro-physical source terms (mainly at homogeneous conditions):
Conclusion (1):
More sophisticated activation according to Segal/Khain with CAMS aerosol-input: Significant impact on clouds and precipitation
ML-emulated parcel model ‘pyrcl’ is promising
Mixed-phase SBM fully implemented: technically working with reasonable results
ICON-SmART: Preliminary results of seamless multi-year simulations of Aerosol and Reactive Tracer emissions with related chemistry and dynamics, aided by ML components
COSMO-PP CAIIR
ART-component of ICON

## Slide 19
Matthias Raschendorfer
EWGLAM/SRNPW, Norrköping-Hybrid 2025
Some recent physics developments in COSMO for the ICON model
Empirical Hyper-Parameterization by Conditional Adaptive Parameter Tuning (APT)
Conclusion (2):
Consideration of dissipation heating
TKE-feedback on Lower Limits of Diffusion Coefficients (LLDC)
Towards Empirical Hyper-Parameterization by Conditional Adaptive Parameter Tuning (APT)
Parameterization of macroscopic sub-grid heterogeneity:
Dissipation heat-source due to conversions from MKE: Significant reduction of temperature-bias at winter time,
particularly along Antarctic coast
Missing link according to STIC-concept
Increases the positive impact from dissipation heating
“Verification-based” adaptations of parameters with DA-increments as predictors
Impact of a missing canopy scheme can partly be emulated:
Significant reduction of cold and moist near-surface bias at late afternoon
Should be extended by ML -> possible hybrid AI-WP approach
COSMO-action ConSAT
Particular DWD initiative